## Slide 1: Digital Electronics & Logic Design

## Slide 2: Topics to be covered:
Asynchronous (ripple) counter
Ring counter
Johnson counter
Shift registers

## Slide 3
All Flip-Flops are in toggle mode.
The clock input is applied.
Count enable = 1.
Counter counts from 0000 to 1111.
4-bit Binary Ripple Counter :

## Slide 4: Divide-by-2, 4, 8 Counters (asynchronous)
Use a toggle flip-flop (J-K connected together)
· the output of the flip-flop “toggles” at every clock pulse
Divide-by-2 counter
NOTE : negative clock pulsed clock
The circuit divides the clock frequency by 2.

## Slide 5: Divide-by-2, 4, 8 Counters (asynchronous)
Divide-by-2, 4, 8 counters can also be designed,
 circuit divides the clock frequency by 2, 4 or 8
Divide-by-n Counters are asynchronous
No common synchronising clock input is applied to all the flip-flops.
Clock is actually used for data in these applications.

## Slide 6: Divide-by-2,4,8 Counter (asynchronous)
Synchronous Counters are distinguished from ripple counters in that clock pulses are applied to the clock inputs of all the flip-flops.
common pulse triggers all flip-flops simultaneously rather than one at a time in succession (as in ripple counter)

## Slide 7
Difference between Asynchronous and Synchronous Counter :
Asynchronous Counter | Synchronous Counter
1. Clock input is applied to LSB FF. The output of first FF is connected as clock to next FF. | 1. Clock input is common to all FF.
2. All Flip-Flops are toggle FF. | 2. Any FF can be used.
3. Speed depends on no. of FF used for n bit . | 3. Speed is independent of no. of FF used.
4. No extra Logic Gates are required. Cost is less. | 4. Logic Gates are required based on design. Cost is more.
1
fmax =
n x tp
1
fmax =
tp

## Slide 8: Example Problem
13 COUNTERS
Page 8
ECEn 224
Design a 3-bit binary counter
The Z output is TRUE iff count value is even
The Y output is TRUE iff count value is multiple of 3

## Slide 9
Counters Based on Shift Register
Mod-4 Ring Counter
The output of LSB FF is connected as D input to MSB FF.
This is commonly called as Ring Counter or Circular Counter.
The data is shifted to right with each clock pulse.
This counter has four different states.
This can be extended to any no. of bits.

## Slide 10
Twisted Ring Counter or Johnson Counter
Mod-8 Johnson Counter
The complement output of LSB FF is connected as D input to MSB FF.
This is commonly called as Johnson Counter.
The data is shifted to right with each clock pulse.
This counter has eight different states.
This can be extended to any no. of bits.

## Slide 11: Shift Registers
Using registers to store, manipulate and transfer data
11

## Slide 12: Definition
A register is a digital circuit with two basic functions: Data Storage and Data Movement
  A shift register provides the data movement function
  A shift register “shifts” its output once every clock cycle
A shift register is a group of flip-flops set up in a linear fashion with their inputs and outputs connected together in such a way that the data is shifted from one device to another when the circuit is active
12

## Slide 13: Shift Register Applications
Communications:
converting between serial data and parallel data.
temporary storage in a processor.
  some arithmetic operations-
  multiply, divide
some counter applications
  Johnson counter
  ring counter
time delay devices
13

## Slide 14: Shift Register Characteristics
14
Types
  Serial-in, Serial-out
  Serial-in, Parallel-out
  Parallel-in, Serial-out
  Parallel-in, Parallel-out
  Universal
Direction
  Left shift
  Right shift
  Rotate (right or left)
  Bidirectional
n-bit shift register

## Slide 15: Data Movement
The bits in a shift register can move in any of the following manners
15

## Slide 16: Data Movement
n-bit shift register
n-bit shift register
16
n-bit shift register
n-bit shift register

## Slide 17: Serial-In Serial-Out
n-bit shift register
Data bits come in one at a time and leave one at a time
One Flip-Flop for each bit to be handled
Movement can be left or right, but is usually only a single direction in a given register
Asynchronous preset and clear inputs are used to set initial values
17

## Slide 18: Shift Registers
The simplest shift register is one that uses only Flip-Flops
The output of a given Flip-Flop is connected to the D input of the Flip-Flop at its right.
Each clock pulse shifts the contents of the register one bit position to the right.
The Serial input (SI) determines what goes into the leftmost Flip-Flop during the shift. The Serial output (SO) is taken from the output of the rightmost Flip-Flop.
18
Q
Q
Q
Q

## Slide 19: Serial-In Serial-Out
A simple way of looking at the serial shifting operation, with a focus on the data bits, is illustrated at right
The 4-bit data word “1011” is to be shifted into a 4-bit shift register
One shift per clock pulse
Data is shown entering at left and shifting right
19
1
2
3
4
5

## Slide 20: Serial-In Serial-Out
The diagram at right shows the 4-bit sequence “1010” being loaded into the 4-bit serial-in serial-out shift register
Each bit moves one position to the right each time the clock’s leading edge occurs
Four clock pulses loads the register
20

## Slide 21: Serial-In Serial-Out
This diagram shows the 4-bit sequence “1010” as it is unloaded from the 4-bit serial-in serial-out shift register
Each bit moves one position to the right each time the clock’s leading edge occurs
Four clock pulses unloads the register
21

## Slide 22: Serial-to-Parallel Conversion
We often need to convert from serial to parallel
  e.g., after receiving a series transmission
The diagrams at right illustrate a 4-bit serial-in parallel-out shift register
Note that we could also use the Q of the right-most Flip-Flop as a serial-out output
22
n-bit shift register

## Slide 23: Serial-to-Parallel Conversion
These two shift registers are used to convert serial data to parallel data
The upper shift register would “grab” the data once it was shifted into the lower register
23

## Slide 24: Parallel-to-Serial Conversion
We usa a Parallel-in Serial-out Shift Register
The DATA is applied in parallel form to the parallel input pins PA to PD of the register
It is then read out sequentially from the register one bit at a time from PA to PD on each clock cycle in a serial format
One clock pulse to load
Four pulses to unload
24
n-bit shift register

## Slide 25: Parallel-In Parallel-Out
Parallel-in Parallel-out Shift Registers can serve as a temporary storage device or as a time delay device.
The DATA is presented in a parallel format to the parallel input pins PA to PD and then shifted to the corresponding output pins QA to QD when the registers are clocked.
One clock pulse to load
One pulse to unload
25

## Slide 26: Universal Shift Register
n-bit shift register
Universal shift register
Can do any combination of parallel and serial input/output operations
Requires additional inputs to specify desired function
Uses a Mux-like input gating
26
L/S
L/S
A
B
A
B
F
1
0
1
0

## Slide 27: Universal Shift Register
Parallel shift register (can serve as converting parallel-in to serial-out shifter):
27