## Slide 1: Hydrosphere
2/3 of our earth is water but 97% of it is saline water
Water is scarce. Our negligence is disturbing the
Sphere of water
Putting our life at stake

## Slide 2: Water quality parameter
Colour
Taste
Odour
Dissolved Oxygen
Dissolved nutrients
Sunlight penetration
Dissolved Oxygen is an important parameter

## Slide 3: Diurnal variation of DO level
Contributing factors:
Respiration
Photosynthesis
Re-aeration
Level of pollution(organic) in the water body

## Slide 4: Water Pollution
Effects the physical and chemical quality of water
Depletes Dissolved Oxygen level in the water body
Effect on human health
Damage to the esthetic beauty
Loss of tourism

## Slide 5: The Pollutants
Oxygen Demanding Waste
  Biodegradable
  Organic or inorganic
Effect of drop of DO:
  Threat to aquatic life
  Damage to aquatic body

## Slide 6: Measurement of DO
Chemical Oxygen Demand (COD)
Biochemical Oxygen Demand (BOD)

## Slide 7
Pathogens
Bacteria
Virus
Protozoa
Helminths/Parasitic worms

## Slide 8
Nutrients
  -Limiting nutrients
  -Nitrogen, Phosphorus, Carbon
Source
Municipal waste, chemical fertilizer, soap, detergent, acid rain, certain bacteria

## Slide 9
Effects:
Excess of algal growth
Dead and decaying organic matter
Fall of DO level
Colour and odour
Excess of nitrogen in water can cause Blue baby syndrome

## Slide 10
Salts (TDS)
  Sources:
  Irrigation drainage water
  Industrial discharge

## Slide 11
Effect:
Salinity problem
If the salinity increases beyond tolerance limit then it is harmful even lead to death
Remedy
Desalinisation

## Slide 12
Thermal pollution
Discharge from thermal power plant, nuclear power plant,
Effect:
Metabolic rate increases with rise in certain degree of temperature but excess temperature raise will lead to death of fish

## Slide 13
Heavy Metal
Pb, Hg, Cr, Co, Cd, As etc.
Effects:
Enzyme inhibition, kidney damage, blurred vision, disorder of liver, brain
Hg poisoning--- Minamata disease

## Slide 14
Pesticides
Volatile organic compounds
  Vinyl chloride
  Tetra chloro ethylene
  Trichloro ethylene
  Carbon tetrachloride

## Slide 15: River and Stream Pollution
Biological Oxygen Demand(BOD)
The aerobic decomposition of waste present in water with the help of microorganism releasing CO₂
unit: mg/l
every effluent has got a BOD value
Anaerobic decomposition releases methane

## Slide 16: Biological Oxygen Demand
BOD₅
Estimation of BOD over a period of 5 day at 20◦C in 300ml stoppered bottle
Seeded BOD₅
Estimation of BOD by diluting with

## Slide 17: Ground Water Hydrology
Aquifer
Ground water reservoir
Two types of Aquifer:
Confined
Unconfined Aquifer

## Slide 18
Hydraulic Gradient
It is the slope of water table
Hydraulic Gradient= Change in head/Horizontal
distance
Darcy’s law
It is the flow of water
Q=KA dh/dl

## Slide 19: Treatment of Water
Surface Water Treatment:
Source Screening Mixing Tank Flocculation
Disinfection Sand filter Settling Tank

## Slide 20: Treatment of Waste Water
Primary Treatment:
Removal of settle able and floatable material
Flocculent particles which aggregate and settles down at the bottom of the tank

## Slide 21
Secondary Treatment:
Trickling Filter
Activated Sludge Process
Rotating Disc Biological Contractor
Sludge treatment
Oxidation Pond

## Slide 22: Hardness of Water
Presence of bivalent metal ion, calcium, magnesium etc. and aluminium, manganus ion are also responsible
Hardness is of two types
Temporary
Permanent
Hardness is expressed in terms of equivalent amount of CaCO₃ present

## Slide 23: Hardness Removal
Temporary Hardness Removal
Boiling & Addition of lime water
in terms of calcium carbonate precipitation
Permanent Hardness Removal
Lime soda process
Base exchange process